## Slide 1: Environmental Impacts of Water Withdrawal: Focus on Salmon Janne Kaje, KC Regional Partnerships Unit & Snoqualmie Watershed Forum

## Slide 2: Topics
Salmon life cycle
  Summer habitat utilization
Water withdrawal effects on habitat
  Habitat quantity & Water quality
Surface water diversion effects on fish
  Screening & Technologies
“Instream Flow”
  Basin closures, seasonal limitations
Reducing impacts of your water use

## Slide 3: Chinook Life Cycle

## Slide 4: Freshwater Juvenile Rearing
Species | Freshwater rearing
Chinook | ~ 2-16 months
Coho | ~ 12 months
Steelhead | ~ 12-24 months
Rainbow trout Cutthroat trout Lamprey | Resident
Coho are most likely to be found in small tributaries during summer months.
Chinook and Steelhead are more likely to be found in larger tributaries or the mainstem river during summer months.

## Slide 5: Stream Flow Pattern in King County
Irrigation Season

## Slide 6: What’s a fish stream?
Farm drainage ditch in Snoqualmie Valley

## Slide 7
400
4,000+ fish recovered from 2,000 feet of “ditch”!

## Slide 8: Habitat Quantity
Juvenile salmon are territorial
Lower flow =
  Fewer territories, more competition
  Lower food production (aquatic and terrestrial bugs)
  Shallower , warmer pools
Extreme case =
  Fish get stranded in isolated, stagnant pools

## Slide 9: Water Quality
Temp
Salmon are cold-water fish
Need cool, clear, well-oxygenated water
High temperature can be lethal
Less Water
Oxygen

## Slide 10: Return Flow Quality
Irrigation return water impacts quality
  Usually WARMER in summer
  Suspended sediment input
    Clog gills and bury gravel substrate
  Nutrient, chemical runoff
Nutrients
Oxygen
Algae bloom

## Slide 11: Pumps & Diversions
Fish can get diverted into fields and stuck on intake screens.
Fish protection is required by state law.
  RCW 77.57.010. Fish guards required on diversion devices — Penalties, remedies for failure.
  RCW 77.57.070. Diversion of water — Screen, bypass required.
In waterways with Endangered Species Act listed fish, could be guilty of “take”.
http://wdfw.wa.gov/conservation/habitat/planning/screening/

## Slide 12: Fish Protection Technology
Many different devices
  Depends on volume, water source, stream gradient
http://www.farmerscreen.org/
http://intakescreensinc.com/

## Slide 13: Fish Protection Technology
Guidance documents and regulations
  Screen mesh size
  Water velocity
  Other design factors

## Slide 14: Water Rights for Fish
“Instream Flows” have been set in many King County rivers and streams.
  Most “Instream Resources Protection Programs” established in 1970’s – 1980’s
  Codified in WAC Title 173
  Priority dates just like out-of-stream rights
    Do not affect senior rights
Many dams and hydroelectric facilities have instream flow requirements (e.g., minimum flow, ramping rates, pulse flows)

## Slide 15: Types of Instream Flows
Snohomish Basin (incl. Snoqualmie) example:
  WAC 173-507
  Semi-monthly minimum flow schedule in major rivers. Multiple “control points”.
  Complete closure to further appropriation in several larger tributaries (e.g., Griffin, Harris, Patterson, Raging)
  Fixed low-flow limit in several small streams (e.g., Langlois, Tate and many unnamed streams).

## Slide 16: Reduce Your (Water) Footprint!
Maintain healthy soil – use less water.
Implement efficient irrigation systems.
Prevent stock washing water from flowing directly to stream.
Maintain vegetated buffers on all water courses.
Reduce fertilizer and pesticide use. Use BMPs for application.
Screen and properly maintain all pumps & diversions.

## Slide 17
Questions?