## Slide 1: Lake Washington PCB/PBDE Study Estimates of loading from major pathways
Curtis DeGasperi, Jenée Colton, and Richard Jack
Science Section
King County Water and Land Resources Division, Department of Natural Resources and Parks
2014 Salish Sea Ecosystem Conference
May 1, 2014

## Slide 2: Conceptual Model for PCBs

## Slide 3: Major Pathways
Rivers (Cedar and Sammamish)
Local Drainages
  Monitored tributaries
    Thornton Creek
    Juanita Creek
    May Creek
  Remaining unmonitored lake drainage
CSOs
Floating bridges (stormwater runoff)
Direct atmospheric deposition

## Slide 4: Loadings Estimates
Concentration X Flow = Loading
Field study mean concentration used, except
Extrapolation approach for unmonitored tributaries
Enhanced CSO data with historical data
Flow
Gauged flow data OR
Estimated

## Slide 5: Correlations with Land Use/Population
%Total Impervious Cover
%Developed pre-1979
Population Density (#/ac)
%Commercial/Industrial Dev pre-1979
tPCB (g/m2-yr)
tPCB (g/m2-yr)
tPCB (g/m2-yr)
tPCB (g/m2-yr)
Notes: 1979 cutoff selected b/c final federal ban on PCBs
Label tributary dots

## Slide 6: Relationship with Historical LandUse?
Notes: 1979 cutoff selected b/c final federal ban on PCBs
Label tributary dots

## Slide 7: Current PCB Loading Estimates
672 g yr-1 to Lake Washington
140 g yr-1 exits Lake Washington
360 g yr-1 to Puget Sound

## Slide 8: PCB Loading Summary
Lake Washington
Lake Union/Ship Canal
360 g
Puget
Sound
4.8 g
110 g
140 g
Bridges 3 g
CSOs 12 g
Rivers 97 g
Local Dr. 450 g
562 g + 110 g = 672 g
672 g – 140 g = 532 g
?
Bridges 1 g
CSOs 58 g
Local Dr. 40 g
672 g

## Slide 9: Current PBDE Loading Estimates
2,023 g yr-1 to Lake Washington
968 g yr-1 exits Lake Washington
990 g yr-1 to Puget Sound

## Slide 10: PBDE Loading Summary
Lake Washington
Lake Union/Ship Canal
990 g
Puget
Sound
25 g
590 g
800 g
Bridges 19 g
CSOs 14 g
Rivers 580 g
Local Dr. 820 g
1,433 g + 590 g = 2,023 g
2,023 g – 800 g = 1,223 g
?
Bridges 5.6 g
CSOs 68 g
Local Dr. 69 g
2,023 g

## Slide 11: Load from Local Drainage Driven by Stormwater
Stormwater is <30% of annual flow in streams BUT
Accounts for 80-90% of annual PCB load from local drainage

## Slide 12: Loadings Conclusions
Appears to be relationship between local tributary PCB areal loading and age and/or type of development
As much as 70% of lake PCB load comes from local tributaries
As much as 80% of local tributary PCB load delivered in stormwater
Lake Washington is a sink for PCB and PBDE

## Slide 13: QUESTIONS?
http://www.kingcounty.gov/environment/watersheds/cedar-river-lake-wa/pcb-pbde-loadings.aspx
Search: lake washington pcb study