## Slide 1
Conservation of Lake Sammamish Kokanee
An Update on Current Science
A Briefing for the City of Bellevue Planning Commission
Hans Berge– King County Department of Natural Resources and Parks
hans.berge@kingcounty.gov
November 4, 2009

## Slide 2: Kokanee Science
To Date:
Spawning ground surveys (annually since 1996)
Food web research within the lake (2002-2005)
Fry trapping on Lewis Creek (annually since 2007)
Current:
Supplementation (Fall 2009)
Tagging study (2009-2010)
Future:
Stream habitat assessment
Project prioritization
Release strategies
Colonization in other spawning streams
Effects of hatchery releases from Issaquah Creek

## Slide 3
Relative weight (Wr) used to measure condition
Species specific values for cutthroat and kokanee (Hyatt and Hubert 2000)
Cutthroat trout Wr was greater during stratification (t-test, p<0,002)
Kokanee Wr was lower during stratification and the DO squeeze (t-test, p<0.001)
Kokanee growth is reduced in the summer

## Slide 4
20% of the lake is
<17°C and >4 mg/L
Optimal habitat is reduced by temp-DO squeeze

## Slide 5: Important Habitats
Streams (spawning and incubation)
  Lewis
  Vasa
Shoreline of Lake Sammamish (early rearing, upstream migration)
  Deltas
    Early rearing of fry
    Predation
Lake Sammamish (rearing and maturation)
  Water Quality
    Phosphorous
    Nitrogen

## Slide 6: Lewis Creek Example
High flows
  Bed stability/mobility
  Infrastructure risk
Floodplain connectivity
  Flood refuge
  Pool formation
  Energy dissipation
Kokanee redd

## Slide 7: Upper Lewis Creek (above I-90)
Erosion, high flows, good riparian condition

## Slide 8: Lower Lewis Creek (below I-90)

## Slide 9: Acoustic Telemetry Project
Project Goals:
  Understand seasonal movement of kokanee in Lake Sammamish
  Monitor spatial and temporal overlap of limnetic predators and prey
  Investigate the effects of thermal stratification, zooplankton density, and diel period on movement of kokanee

## Slide 10: Hydrophone Deployment

## Slide 11
Limnology
Limnological Measurements
  Temperature, DO
  Light and turbidity
  Secchi Depth
  Monthly zooplankton
Monitoring Buoys (Temp, DO)
SCAMP (Temp and Light)
Secchi (transparency))
Clarke-Bumpus zooplankton sampler

## Slide 12: Fish Collection
TU anglers helped catch fish
Careful handling
Transferred to livewell

## Slide 13: Acoustic Tagging
Boat
Processing Table
Anesthetic
Length and Weight
Tag inserted
Sutures to close incision
Recovery in insulated tank and released

## Slide 14: Results to Date
Analysis in progress…
35 tagged fish
Downloaded data every other month beginning in August
Have heard from 33 fish
Detections at all 4 stations near Bellevue shoreline (and all but one other station)
Kokanee adults found in littoral and limnetic zone of Lake Sammamish