## Slide 1: Flow-Ecology Relationships and Applications to Stormwater Management
Curtis DeGasperi
King County DNRP, WLRD
University of Washington
Hydraulic Design for
Environmental Engineering
March 9, 2021
Notes: Questions during presentation welcome. This is a whirlwind tour of the kind of work we do plus some historical background and context.

## Slide 2: Human Impacts on Water Cycle
Land cover change
  Forest clearing/Development
~1880
Notes: Historically dense tree canopy and accumulation of soil organic matter that stored lots of water. Now (using downtown Bellevue in 1996 as an example) we have impervious roads, rooftops, parking lots and compacted grassy areas that don’t store much water and generate runoff quickly.

## Slide 3: Stormwater Hydrology 101
Vegetation clearing
Soil compaction/removal
Ditching and draining
Covering of land with impervious roofs and roads
  Results in loss of soil moisture and infiltration capacity and conversion of subsurface runoff and long time-scale release to rapid overland runoff and immediate discharge to stream.
  Peak flows can be increased by a factor of 2 to 5 (Hollis, 1975)
  Duration of any flow magnitude longer by factor of 5 to 10 (Barker et al, 1991)
  Forested Q10 becomes Q2 under developed conditions (Booth and Jackson, 1997)
  A 1% increase in impervious cover results in a 3.3% increase in annual flood magnitude (Blum et al, 2020)
Notes: Loss of soil moisture storage and infiltration capacity. Loss of canopy interception. Increased efficiency of transfer of rainfall to stream through connected (effective) impervious cover. Not possible to compare conversion of primarily subsurface flow to a point discharge if converted to conveyance and pond treatment. Compounded by potential increases in extreme precipitation due to climate change.

## Slide 4: Converting Forest to Developed Cover Can Alter Hydrology
Burges et al. 1998. Hydrological Effects of Land-Use Change in a Zero-Order Catchment. J. Hydrologic Engineer. 3(2):86-97.
Notes: The effect of conversion of forest to developed land can be demonstrated with observational data.

## Slide 5: Converting Forest to Developed Cover Can Alter Hydrology
Novelty
Klahanie

## Slide 6: Converting Forest to Developed Cover Can Alter Hydrology
Developed
Undeveloped
Notes: Normalized by basin area. Daily mean flow and daily instantaneous peak flow. There are more peaks and the magnitude of peaks substantially increased under developed conditions. Note that almost no summer peaks are generated in the forested basin.

## Slide 7: Stormwater Management Paradigm
Time Period | Paradigm | Description
Prior to ~1979 | Drainage Efficiency | Convey water downhill as efficiently as possible
1979 – Now | Reduce New Impacts | Reduce harm from new construction with flow control and treatment
Future | Reduce New and Existing Impacts | Capture, infiltrate, detain and treat stormwater everywhere to protect and rehabilitate receiving waters

## Slide 8: Stormwater Mitigation History
Peak standard – Rational Runoff Formula (1979)
Peak standard – SCS curve-number methodology (1990)
Duration standard – Continuous flow modeling (1998)
  Threshold discharge for bed disturbance
  Point discharge from spatially distributed subsurface runoff
  Aggregate duration matching (pre- and post-development)
  Exemption of rural-zoned development from detention requirements
Booth et al. (2002). Forest cover, impervious-surface area, and the mitigation of stormwater impacts. JAWRA 38(3).
Notes: Duration standard designed to maintain channel stability but implies a compromise…that there is an average of protection across the County. A much more expensive/intensive approach would be a reach-specific channel stability analysis. Definitely doesn’t protect sand-bedded streams.

## Slide 9: When and where development occurred important
Before ~1990, little or no flow control
Between ~1990-2000, inadequate flow control
After ~2000 modern flow control requirements
And there are limits to stormwater mitigation
  Development threshold exceptions
  Subsurface flow becomes point source
  Runoff volume generally increases
  Substrate variability is not explicitly addressed
Notes: Point out Lewis and Laughing Jacobs creeks

## Slide 10: Stormwater is a big deal!
Jeff Burkey. November 28, 2018. Updated Estimate of the Annual Average Volume of Treated and Untreated Stormwater
Runoff from Developed Lands in King County. Technical Memorandum to Josh Baldi, WLR Division Director.

## Slide 11: Available data
Lewis Creek (63a)
Laughing Jacobs Creek (15c)
Zackuse Creek (15i) *
Ebright Creek (15h)
Issaquah Creek (12121600)†
King County gages
USGS gage†
* Zackuse gage funded by City of Sammamish
† Partially funded by King County
Notes: Four active continuous King County stream flow gages. There is also a USGS gage near the mouth of Issaquah Creek. Focus on smaller kokanee creeks.

## Slide 12: Look at three factors
Basin Area
Impervious Area
Lewis
Laughing
Jacobs
Ebright
Zackuse
Annual Precipitation
45-50 inches

## Slide 13
Annual flood frequency analysis
Timing of peaks not always the same across streams
Missing data can make it difficult to be certain that annual peak was recorded
Even more difficult for smaller periods of interest – season or month
Need at least 10+ years
Laughing Jacobs and Lewis Creeks
Water Year 2018

## Slide 14: Laughing Jacobs Creek
February 2020 peak for Water Year 2020
Annual maximum Q in February 2020
~ 9 year return period (11% annual exceedance prob)

## Slide 15: Flow duration curves (Lewis and Laughing Jacobs)
Based on 15-minute data collected Oct 1, 1999 to Oct 1, 2019
Discharge
Runoff depth
2-yr
10-yr
Lewis
Laughing Jacobs
Lewis
Laughing Jacobs
Lewis Creek generates more runoff than Laughing Jacobs even after adjusting for differences in drainage area

## Slide 16: Modeled Flow Duration for Laughing Jacobs
2-yr
10-yr
Current (~1990s)
Forested
Caution: All models are wrong
Modeled Laughing Jacobs Creek “Current” 2-yr peak of 120 cfs is greater than the 10-yr “Forested” peak of 73 cfs
Forested 10-yr/Current 2-yr = 73/120 = 0.60
“Current”
“Forested”
Notes: Take home: Laughing Jacobs Forested 10-yr/Current 2-yr = 73/120 = 0.60

## Slide 17: Recall from Booth and Jackson (1997)….

## Slide 18
Timing
Duration
Magnitude
Frequency
Rate of Change
1997

## Slide 19: Altering hydrology (among other things) can alter biology
May et al. 1997. Quality Indices for Urbanization Effects in Puget Sound Lowland Streams. University of
Washington, Seattle, WA. Water Resources Series Technical Report No. 154.
1997

## Slide 20: Konrad (2000), Morley (2000), Konrad and Booth (2002)
2000-2002

## Slide 21: Morley and Karr (2002), Booth et al. (2004)
2002-2004

## Slide 22: Booth et al. (2004) Reviving urban streams: land use, hydrology, biology, and human behavior

## Slide 23: Booth et al. (2004) Reviving urban streams: land use, hydrology, biology, and human behavior

## Slide 24: King County Normative Flow Studies
Notes: At about the same time as

## Slide 25: Normative Flow Concept
Can we develop a valid and defensible small stream flow assessment method using Normative Flow concepts for application to flow management issues in King County?
Adapted from King County Normative Flow Studies web page – bullet one
https://www.kingcounty.gov/services/environment/watersheds/general-information/normative-flow-studies/products.aspx

## Slide 26: What is “Normative Flow” aka “Natural Flow Regime”
Not an attempt to return the landscape to pre-European conditions
However…
historical conditions give us clues to flow regime that native biota were adapted to

## Slide 27: Normative flow principles
Flow is a major determinant of stream habitat, which in turn is a major determinant of biotic composition.
Aquatic species have evolved life history strategies primarily in direct response to natural flow regimes.
Maintenance of natural patterns of longitudinal and lateral stream connectivity is essential to the viability of many aquatic species.
Adapted from: Bunn and Arthington (2002)

## Slide 28: Challenges
Direct observations of the pre-disturbance flow regime are generally unavailable.
Co-located hydrological and biological (or chemical) observations are rare.
Few “reference” streams available.
Covariation of land development and natural landscape features.
How to incorporate climate variability?

## Slide 29: Requirements
Can be calculated annually
Component metrics chosen to minimize redundancy
Demonstrated trend with time (low interannual variability)
Correlated with land cover metrics
Correlated with biological metrics
Relatively unaffected by basin area/elevation/precipitation totals

## Slide 30: Assumptions
Biological response occurs over multi-year time scales
Biota will respond to “normative flow” restoration (reversibility)
A “Normative” hydrologic index will require the use of models to estimate the historical flow regime

## Slide 31: Models
Ability to predict mean annual flow
Ability to predict hydrologic metrics
Account for climate variability
Extrapolate to ungauged locations

## Slide 32: Hydrologic Metrics
Magnitude
  7-day average annual minimum flow
Duration
  Low and high flow pulse duration
  Low and high flow pulse range
  Fraction of year mean annual flow exceeded (TQmean)
Frequency
  Flow reversals
  Low and high flow pulse counts
  Fall and rise counts
Timing
  Date of annual daily minimum flow
Rate of Change
  Rise and fall rates
Richards-Baker Flashiness Index
TQmean

## Slide 33: Hydrologic Metric Calculations
High and Low Flow Pulses
TQmean
R-B Index

## Slide 34
High Flow Pulses
Low Flow Pulses
Long-term mean flow
0.5 x mean flow
2 x mean flow

## Slide 35
High Flow Pulses – Current Conditions
2 x mean flow
21 Pulses

## Slide 36
Low Flow Pulses – Current Condition
0.5 x mean flow
6 Pulses

## Slide 37: Hydrologic Metric Calculations
High and Low Flow Pulses
TQmean
R-B Index
Rise and Fall Rate
Rise and Fall Count
Mean annual flow
Number of days mean annual flow is exceeded
FLOW
DAYS
WATER YEAR
Notes: TQmean is lower in urban streams due to increased storm flow volume, rapid recession rates, and lower wet-season base flow.

## Slide 38: Hydrologic Metric Calculations
High and Low Flow Pulses
TQmean
Richards-Baker Index
Rise and Fall Rate
Rise and Fall Count

## Slide 39: Benthic Index of Biological Integrity
Taxa Richness and composition
  Total number of taxa
  Number of Ephemeroptera (mayfly) taxa
  Number of Plecoptera (stonefly) taxa
  Number of Trichoptera (caddis fly) taxa
  Number of long-lived taxa
Tolerance
  Number of intolerant taxa
  Percent of individuals in tolerant taxa
Feeding Ecology
  Percent of individuals that are predators
  Number of clinger taxa
Population attributes
  Percent dominance (top 3 taxa)
Response to Human Dist.
  
  
  
  
  
  
  
  
  
  

## Slide 40
Tricoptera (caddis flies)
Ephemeroptera (mayflies)
Plecoptera (stone flies)
EPT Taxa

## Slide 41: B-IBI “Calibration”
% TIA
% Dominance
1
3
5

## Slide 42: DeGasperi et al. (2009) Linking hydrologic alteration to biological impairment in urbanizing streams of the Puget Lowlands
2009

## Slide 43: Eight Candidate Metrics
High Pulse Count
High Pulse Range
High Pulse Duration
Low Pulse Count
Low Pulse Duration
TQmean
R-B Index
Flow Reversals

## Slide 44: Hydrologic Metrics Highly Correlated With Each Other (and %imperviousness)

## Slide 45: Hydrologic metrics correlated with B-IBI (n = 16)
HIGH PULSE COUNT (71%)
R-B Index (49%)
TQmean (47%)

## Slide 46: CAUTION! Correlation does not equal causation.

## Slide 47: Hydrologic Metrics Respond to Basin Urbanization over Time
R-B Index
TQmean
HPC
USGS Mercer Creek Bellevue, WA

## Slide 48: Miller Creek Basin Plan Case Study

## Slide 49
TQmean
Fully-Forested
Current Conditions
25th and 75th Percentiles
1949-2002
1949-2002
Degree of Hydrologic Alteration Range of variability approach

## Slide 50
Degree of Hydrologic Alteration
TQmean
High
Medium
Low

## Slide 51: WRIA 8 Status & Trends Boosted Regression Tree Models
HPD
HPC
RBI

## Slide 52: WRIA 8 Status & Trends n = 28
Venema Creek
North Creek

## Slide 53: City of Bainbridge Island (2015)
B-IBI 0-100
HPC
TQmean
RBI
%Development
%Forest

## Slide 54: Necessary, but not necessarily sufficient
Organic pollution index
Fine sediment index
Metals tolerance index
Reference

## Slide 55
Above HPC of ~12
almost guaranteed
to have BIBI less than
35 (10-50 scale)
ceiling
Below HPC of ~12
B-IBI scores can range from 10 to more than 35 (10-50 scale)
Necessary, but not necessarily sufficient

## Slide 56: SAM 2015 small streams study Most important stressors for B-IBI scores…
Stream Health Category | Significant Stressors
Land cover | Watershed Canopy Cover Riparian Canopy Cover Percent Urban Development
Water | Total Nitrogen Total Phosphorus
Sediment | Total Zinc Substrate Embeddedness Substrate Particle Diameter

## Slide 58: Stormwater Management Applications
Juanita Creek Stormwater Retrofit
WRIA 9 Stormwater Retrofit Study
Bear Creek Watershed Management Study

## Slide 59: What Are Stormwater Retrofits
Construction projects to control stormwater
Locations that have previously been developed
Sited where existing stormwater controls are inadequate
Not part of redevelopment

## Slide 60: Why are Retrofits Important?
Most developed areas have no or inadequate controls
Large storm flows erode streams
Untreated stormwater harms fish
Retrofits improve flow and water quality

## Slide 61: Stormwater Retrofit Examples
Ponds
Bioswales
Check Dams
Cisterns
Pervious Pavement
Rain Gardens
Green Roofs

## Slide 62: Juanita Stormwater Retrofit Study

## Slide 63: Juanita Creek Stormwater Retrofit

## Slide 64: WRIA 9 Stormwater Retrofit Study
Notes: Discuss project goals and demostration of SUSTAIN application

## Slide 65: Project Area
WRIA 9 except
  Headwaters above Howard Hanson Dam (forested)
  City of Seattle (combined system)
  Vashon Island
Focus on streams

## Slide 66: SUSTAIN: System for Urban Stormwater Treatment and Analysis INtegration
U.S. EPA model developed to assist stormwater managers in selecting cost-effective stormwater BMPs to meet watershed goals.
Source: EPA
Model Inputs:
BMP Design and Cost Assumptions
Flow or water quality goals

## Slide 67: What is SUSTAIN?
An ArcGIS-based framework designed to support evaluation and decision making:
  How effective are green and/or gray treatment BMPs in reducing runoff and pollutant loadings?
  What are the most cost-effective BMP options to meet specified water quantity and quality objectives?
http://www2.epa.gov/water-research/system-urban-stormwater-treatment-and-analysis-integration-sustain
Notes: A bit more on what SUSTAIN is for….emphasizing cost-effective approach for meeting specified water quantity and/or water quality targets
Applications across the U.S.

## Slide 68: SUSTAIN Applications
Los Angeles County, CA
Upper North Branch Oak Creek, MI
Little Rocky Run, VA
Kansas City, MO
Louisville, KY
http://www.epa.gov/nrmrl/wswrd/wq/models/sustain/#Downloads
Notes: SUSTAIN has been applied in stormwater and CSO control management studies at a number of locations throughout the US. I can point anyone that is interested to these documents if you provide me your contact information during the break or after the workshop.
Although SUSTAIN has been applied successfully in a number of studies, we admittedly have had some difficulty working through

## Slide 69: Data Needs
Land Use/Land Cover map in GIS
Watershed model
  Internal model in SUSTAIN
  External model (Examples: HSPF, SWMM)
BMP types, design configurations, costs
Instream targets
Notes: Overview of data needs, emphasizing that we are using the External Model option in SUSTAIN…HSPF watershed model…and that we have most of what we need at this point:
2007 Land Use/Land Cover from University of Washington Urban Ecology Research Laboratory (UERL)
Stream network and HSPF watershed models
Instream targets
But we still need inputs on BMP types, design configurations, and costs
Today we are looking for input on BMP types
Design configurations and costs will be the work of the project technical team

## Slide 70
Notes: I want to say something about scale because the scale of the application (or really the project goal) determines which approach is feasible within the time and resource constraints of this project
We are interested in coming up with stormwater retrofit cost estimates for most of WRIA 9 below Howard Hanson Dam and extrapolating costs to the Puget Sound basin. A site specific analysis that explicitly simulates BMPs at every household, road, or parking lot is not feasible. SUSTAIN offers what is called an Aggregate BMP approach that allows the use of scalable BMPs on a reasonable sub-basin scale.

## Slide 71: Two Optimization Options
Scatter Search – minimize cost to achieve multiple objectives (e.g., flow and water quality)
NSGA-II – Non-dominated Sorting Genetic Algorithm II to develop a cost-effectiveness curve based on a single objective

## Slide 72: Cost-Effectiveness Optimization
Chart: Cost ($ Million)
Cost-Effectiveness Curve | 0 | 0.024816 | 0.085478 | 0.085478 | 0.19577 | 0.2068 | 0.24449 | 0.2454 | 0.32996 | 0.32996 | 0.36765 | 0.36765 | 0.3989 | 0.41268 | 0.42555 | 0.43658 | 0.43934 | 0.46691 | 0.48897 | 0.51011 | 0.5386 | 0.54688 | 0.54779 | 0.54871 | 0.54871 | 0.54963 | 0.54963 | 0.55055
Selected Solution | 0.54688 | 0.54688 | -1
Selected Solution | 0.54688 | 0.54688 | -1
Cost in Millions of Dollars
Effectiveness (%Reduction)

## Slide 73: Cost-Effectiveness Optimization
Chart: Effectiveness (% Reduction)
| 0 | 2.481618E-2 | 8.5477940000000002E-2 | 8.5477940000000002E-2 | 0.19577206 | 0.20680146999999999 | 0.24448529000000044 | 0.24540441000000043 | 0.32996324000000032 | 0.32996324000000032 | 0.36764706000000008 | 0.36764706000000008 | 0.39889706000000086 | 0.41268382000000031 | 0.42555147000000032 | 0.43658088000000111 | 0.43933824000000032 | 0.46691176000000056 | 0.48897059000000087 | 0.51011028999999886 | 0.53860293999999997 | 0.54687500000000111 | 0.54779412000000005 | 0.54871323999999999 | 0.54871323999999999 | 0.54963234999999899 | 0.54963234999999899 | 0.55055147000000004
CISTERN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
WETPOND | 0 | 0 | 0 | 0 | 1.0487 | 1.0487 | 1.0487 | 1.0487 | 2.0974 | 2.0974 | 2.0974 | 2.0974 | 3.146 | 2.0974 | 4.1947 | 2.0974 | 1.0487 | 2.0974 | 2.0974 | 1.0487 | 2.0974 | 3.146 | 4.1947 | 6.2921 | 6.2921 | 6.2921 | 6.2921 | 2.0974
RAINBARREL | 0 | 0.55188 | 0 | 0 | 0 | 0 | 0 | 0.18396 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
BIORETENTION | 0 | 0.18912 | 0.75648 | 0.75648 | 0 | 0.18912 | 0.75648 | 0.75648 | 0 | 0 | 0.75648 | 0.75648 | 0 | 1.7021 | 0 | 2.5103 | 4.2124 | 3.2668 | 5.2097 | 6.7226 | 6.7226 | 6.7226 | 6.7226 | 6.7226 | 6.7226 | 6.7226 | 6.7226 | 14.2535
POROUSPAVEMENT | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.77355 | 0.77355 | 0 | 0 | 0 | 1.5471 | 1.5471 | 4.6413
 | 25
Effectiveness (%Reduction)
Cost in Millions of Dollars
Chart: 
 | 0 | 3.146 | 0 | 6.7226 | 0.77355

## Slide 75
50 gallon rain barrel
$220 unit cost including construction
$ 85.40 per yr I&E
O&M assumed negligible
Total Present Value unit cost =
$1,533
~3,000 gallon cistern
$1,600 unit cost including construction
$ 85.40 per yr I&E
O&M assumed negligible
Total Present Value unit cost =
$2,913
Residential On-site Detention Facilities
30-yr lifecycle cost assuming 5% discount rate

## Slide 76
Bioretention Facilities
1 Unit is 100 ft2
$20/ft2 Design, permitting, and construction
Rain Garden
$ 1.10/ft2-yr O&M
$213.50 per yr I&E
TPV cost = $69.73/ft2
Roadside Bioretention
$ 1.10/ft2-yr O&M
$170 per yr I&E
TPV cost = $63.04/ft2
30-yr lifecycle cost assuming 5% discount rate

## Slide 77
Porous Parking Areas
1 Unit is 100 ft2
$ 20/ft2 design, permitting, and
construction
$ 0.02/ft2 O&M
$427.00 per yr I&E
TPV = $85.95/ft2
30-yr lifecycle cost assuming 5% discount rate

## Slide 78
Detention Pond
1 Unit is ~13,000 ft3
$ 3.43/ft3 construction cost
$ 1.20/ft3 design and permitting
$ 0.01/ft3 O&M
TPV Cost = $ 25.81/ft2
or $ 4.78/ft3
Land cost = $18.25 ft2
30-yr lifecycle cost assuming 5% discount rate

## Slide 79
Modeling Approach
Study area: 278 mi2, 446 catchments
Model 135 hypothetical 100-acre catchments representing combinations of:
  5 generic land uses
  3 soil types
  2 slopes
  3 precipitation zones
  2 land costs
Notes: This is a modeling project.
We modeled different factors that influence the size and type of stormwater retrofits, such as…
Scaled the results to the project area and extrapolated to puget sound

## Slide 80: SUSTAIN Optimization Target: Reduce Stream Flashiness
High Pulse Count (HPC): Number of times mean daily flows ≥
high-flow threshold set at 2 X long-term mean daily flow rate
Notes: Hydrologic indicator that can provide link to biological health

## Slide 81: Indicators,Targets and Goals
Horner, R.R. 2013. Development of a Stormwater Retrofit Plan for Water Resources Inventory Area 9: Flow and Water Quality Indicators and Targets. King County Water and Land Resources Division, Seattle, Washington.

## Slide 82
SUSTAIN
Output
Each point represents
a possible BMP strategy
Chart: Cost ($ Million)
Cost-Effectiveness Curve | 11 | 10.9 | 10.7 | 10.5 | 10.4 | 9.9 | 9.9 | 9.6 | 9.5 | 9.4 | 9.2 | 9 | 8.8 | 8.7 | 8.2 | 8.1 | 8 | 8 | 7.8 | 7.8 | 7.6 | 7.5 | 7.4 | 7.4 | 7.3 | 7.2 | 7.1 | 7.1
Selected Solution | 7.1284 | 7.1284 | -1
Selected Solution | 7.1284 | 7.1284 | -1
Chart: Cost ($ Million)
Cost-Effectiveness Curve | 0.31817 | 0.32073 | 0.3259 | 0.33115 | 0.33381 | 0.34744 | 0.34744 | 0.35588 | 0.35874 | 0.36162 | 0.36745 | 0.37338 | 0.3794 | 0.38245 | 0.39805 | 0.40125 | 0.40447 | 0.40447 | 0.411 | 0.411 | 0.41763 | 0.42098 | 0.42436 | 0.42436 | 0.42777 | 0.43121 | 0.43467 | 0.43467
Selected Solution | 0.43368 | 0.43368 | -1
Selected Solution | 0.43368 | 0.43368 | -1
HPC
B-IBI

## Slide 83: Modeled Infrastructure Needs
Average of 2.5 inches of storage needed throughout the watershed to improve stream flow and water quality to fully forested conditions
Big range based on amount of impervious area
  Up to 4 inches in urban areas
  As little as 0.1 inches in rural areas
Hydrology has potential to support good to excellent BIBI scores
Notes: Storage is amount of runoff needed to be captured by stormwater facilities to meet optimization target
More storage needed in urban areas, less in rural areas
B-IBI

## Slide 84: Annual Public Costs: WRIA 9 Project Area
 | 30-year | 100-year
Annual Capital Costs | $210M | $46M
Annual Operating Costs* | $650M | $540M
*Operating costs include O&M and I&E costs. Value reflects annual operating costs after all necessary facilities are built.

## Slide 85: Annual Public Costs: Puget Sound Basin
*Operating costs include O&M and I&E costs. Value reflects annual operating costs after all necessary facilities are built.
 | 30-year | 100-year
Annual Capital Costs | $4.3B | $650M
Annual Operating Costs* | $13B | $11B

## Slide 86
https://www.kingcounty.gov/services/environment/watersheds/sammamish/bear-creek/bear-creek-stormwater-plan.aspx

## Slide 87: Bear Creek Watershed Management Study

## Slide 88
Bear Creek Watershed Management Study

## Slide 89: Current trends – King County – 46 Stations 2000-2020 with at least 15 years of data
slope
Fraction of sites with trend slope less than or equal to

## Slide 90: Current hydrologic trends – King County – 46 Stations 2000-2020
McBride, G.M. 2019. Has water quality improved or been maintained? A quantitative assessment procedure. J. Env. Qual. Doe:10.2134/jeq2018.03.0101.
Notes: Bayesian Credible Intervals on slopes to determine the probability that the slope is not zero

## Slide 91: USGS Mercer Creek, Bellevue, WA (12120000 )
1937
1996
Kelsey Creek (08EAS2272)

## Slide 92: USGS Mercer Creek, Bellevue, WA (12120000 )
1937
1996

## Slide 93: USGS Mercer Creek, Bellevue, WA (12120000 )
1937
1996
Kelsey Creek (08EAS2272)
B-IBI 0-100 Score
2005
2010
2015
2020

## Slide 94: Current B-IBI trends – King County 119 Stations 2000-2020 with at least 15 years of data
Fraction of sites with trend slope less than or equal to
slope

## Slide 95: Current B-IBI trends – King County – 119 Stations 2000-2020
McBride, G.M. 2019. Has water quality improved or been maintained? A quantitative assessment procedure. J. Env. Qual. Doe:10.2134/jeq2018.03.0101.
Notes: Bayesian Credible Intervals on slopes to determine the probability that the slope is not zero

## Slide 96: Southern California leading the way…

## Slide 97: Some other interesting efforts…

## Slide 98: King County Organization
Department of Natural Resources & Parks
Water and Land Resources Division

## Slide 99: Water and Land Resources Division
Environmental Laboratory
Science and Technical Support
Rivers and Floodplain Management
Rural and Regional Services
Stormwater Services

## Slide 100: Science and Technical Support Section
Me

## Slide 101
Swan Creek, Tacoma, Washington
Questions?

## Slide 102: Thank you.
Curtis DeGasperi, Lead Hydrologist curtis.degasperi@kingcounty.gov; (206) 477-4677 Water and Land Resources Division
King County Department of Natural Resources and Parks
Notes: Questions?

## Slide 104
Booth et al. 2002 (JAWRA)
Burges et al. 1998 (JHydEng)