## Slide 1: Beyond urban streams: impacts to stream health in forested basins.
Beth Sosik, King County
October 2022
Notes: What I’ll be talking about today is a study I recently conducted looking at how forest conditions interact with stream health in forested basins, specifically how timber harvests can influence those interactions.

## Slide 2: Study Objectives
Puget Sound Partnership’s Freshwater Strategic Initiative
  Draft Working Lands Strategy
Biotic Integrity  Benthic Index of Biotic Integrity (B-IBI)
Study Questions:
Do forest conditions influence biotic integrity?
What mechanisms and spatial scales?
Notes: This study sought to get better understanding of the relationships between forest management practices in the Puget Sound area and stream biotic integrity as measured by the benthic index of biotic integrity, also known just as the B-IBI.
The B-IBI is based on the stream macroinvertebrate community. It’s a single score that integrates the diversity and relative abundance of taxa that are sensitive to degraded conditions.
The primary study questions were first: Do forest conditions influence biotic integrity, and then, if so, what are the main mechanisms and spatial scales of that effect?

## Slide 3: Rationale
Undeveloped basins have best potential B-IBI scores
But lots of underperforming scores!
303(d) Impairment listing at 65 in Puget Lowlands
Forest Harvest?
Impairment criterion
Notes: Just to give some background rationale for why we did this study. There is a well-established relationship between biotic integrity as measured by the B-IBI (here on the Y-axis) and the proportion of a basin that has been developed (here on the x-axis).
The blue line in this figure is the 90th percentile of this relationship, and it represents the best case score we would expect at a given level of development, we’ll refer to that here as the biological potential.
We tend to see better scores, and better biological potential, in basins that are less developed (here on the left hand side of the figure).
But even under very low levels of development, variability in scores is quite large, and we see a lot of sites that are underperforming relative to their potential.
And this has regulatory consequences. In the Puget Lowland ecoregion, one of the criteria for 303(d) impairment listing is an average B-IBI score of 65 or less in the two most recent years of sampling.
Furthermore, in a 2019 study that we conducted, we characterized basins with excellent biotic integrity, and found that these basins typically had at least 72% forest cover in their contributing basins.
This raises the question of whether forest harvests and tree removal can create conditions that impair streams in undeveloped basins. This question has been raised in many previous studies, with conflicting results. And the array of studies and conflicting results indicates that there is a complex and mixed response that may involve other factors.

## Slide 4: Approach
Structural Equation Model (SEM)
  Holistic look at streams as a system
    Forests, streams, and physical conditions.
132 forested basins with minimal urban development
Retrospective analysis
  Leverage existing B-IBI data and spatial datasets
  Relied heavily on modelled retrospective data
Notes: And so for this study, to try to do things a little bit differently and to try to incorporate those potential other factors, we took an approach that used structural equation modelling.
Structural equation modelling is many things, but in the context of this study we can think of it as both a statistical tool and an analytical framework for investigating systems.
And we hoped that by using it in this study, we could get a more holistic look at streams as a system, a system composed of the forests surrounding the streams, the in-stream processes, as well as the physical conditions of the contributing basin.
We focused our efforts on forested stream basins in the Puget Sound basin. These were basins that had > 70% vegetated cover, <10% urban development, and they also passed visual checks of other non-forestry related land uses that thought might impact scores (for example, mines in the basin, or major roads very close to the sampling point).
We also decided to leverage existing B-IBI and spatial datasets for a retrospective analysis, with the hope that we would have a larger dataset and hopefully a more powerful analysis.
We obtained B-IBI data from multiple agencies across the Puget Sound Basin from the Puget Sound Stream Benthos website.
We also relied heavy on modelled spatial datasets for our explanatory variables. These datasets were both spatially explicit to our sampling points and temporally explicit to each of our samples.
So for example, we could get annual landcover change, forest conditions, soil characteristics, stream temperature and flow for a specific site and for a specific point in time.

## Slide 5: Modelled Data Fine Sediment
3 different methods
    Biological Sediment Tolerance Index (BSTI)
    Fine Sediment Biological Index (FSBI)
    Inferred Sediments (bio.infer)
  Sediment impacts inferred from macroinvertebrate community
Notes: We also had to use estimated fine sediment values in this study, because we weren’t able to obtain empirical data for all of our B-IBI samples. And so we used three different methods: the BSTI, the FSBI, and another method called bio.infer.
All three methods infer fine sediment impacts from the macroinvertebrate community present in our sample.
Obviously empirical data would be much better, but in the absence of that, we can think of this as fine sediment impact from the bug’s point of view.
We used all three methods to incorporate some uncertainty that might come with using each method individually.

## Slide 6: Approach
Riparian areas at multiple scales:
Three widths
  50’
  100’
  Site Potential Tree Height (median 200’)
Two upstream extents
  Total riparian area
  100m sample reach
Notes: Continuing on with our approach, we wanted to explore how distance from the stream might mediate the influence that forest conditions have on stream conditions.
We ran our analyses using three different riparian buffer widths extending from either side of the stream. These widths were picked based on either current or proposed regulatory considerations.
The 50’ and 100’ buffers were fixed width. The third buffer was a variable width, and it was based on site potential tree heights. This buffer varied between 100 and 260 feet wide, with a median value of 200’ wide.
In addition, we also wanted to explore the relative impacts resulting from forest conditions in the immediate sample reach, vs impacts resulting from forest conditions in the total riparian area upstream.
Looking at this figure we can see our sample point represented by the red star.
The whole stream network in the basin has the three buffers applied: 50’, 100’ and site potential tree height buffers. Those were used to obtain spatial data for the whole upstream extent of the riparian area.
And then in just the 100 meters upstream of our sampling point is the sampling reach zone, with each of the three buffers applied: 50’, 100’ and site potential tree height buffers.

## Slide 7: Hypothesized routes for impact
Forest Harvest
Forest Conditions
In-stream Stressors
B-IBI
Stream Temperature, Trophic Structure, Baseflows, Stormwater Flows, Fine Sediment, Chemical Applications
Canopy Cover, Basal Area, Slope, Stand Height, Stand Age, % Sand
Shading, Debris inputs, Runoff, Evapotranspiration, Erosion
Notes: Our hypothesis ,in a very simplified schematic, was that forest harvests create forest conditions that affect in-stream stressors that, in turn, affect B-IBI.
Because getting details of actual forest harvests going back multiple decades is extremely difficult, we focused on forest conditions that can be directly altered by forest harvest, or that may influence recommendations for management practices.
Some of the roughly three dozen conditions we looked at include canopy cover, basal area, slope, etc.
Before I move on, I want to point out that one of the features of structural equation modelling is that it allows us to use variables that are potentially correlated as long as there’s a reasonable assumption of some causal pathway. As an example, canopy cover, basal area, stand height and stand age could all share a common cause of forest stability.
We theorized that these forest conditions altered various natural processes, such as shading or debris inputs, that in turn impacted in-stream conditions or stressors, such as stream temperature, trophic structure, etc.
These in-stream stressors were six different pathways that we hypothesized were likely to directly influence B-IBI scores.
You’ll see that chemical applications (such as the use of fertilizers or pesticides) is crossed out, and that is because we not able to locate reliable data on location, type and timing of chemical applications in these basins. And so we kept this node in our conceptual framework because we felt that it was very important, but we were not able to actually include it in our analysis.

## Slide 8: Main Findings
Model could not be validated, these are exploratory results
Riparian forest conditions had little total effect on B-IBI scores
Effect size decreased as distance from stream increased.
Effects occurred at both stream reach and total riparian scales
  Stronger effect from total riparian conditions
Fine sediment from any source had a larger effect on B-IBI
Notes: With our results, there was a lot to unpack, and really too much to unpack here, so I’m going to skip ahead to the main findings.
But before that I want to preface that our model could not be validated because we did not have an additional validation dataset. As a result, these are exploratory results, we need to take them with a little grain of salt, but even so, the implications of the results are worthy of consideration and discussion.
With that being said, the first and biggest main finding is that riparian forest conditions had very little total effect on B-IBI scores. It was statistically significant, but ecologically very small. We’re talking about the difference of 1-2 B-IBI points between basins with good, mature riparian forest cover and basins with sparse, young riparian forest cover.
The next big take-home was that effect size decreased as distance from the stream increased. We saw the biggest effect size using our 50’ stream buffer, and then moving out to our 100’ buffers, the effect size was about half of what we saw using our 50’ buffers. Then using the site potential tree height buffers, which were the widest set, with that dataset we could no longer achieve good model fit because the data were just too noisy. I felt that was a pretty surprising finding.
Next we found that, in the effects that we did see, occurred at both the stream reach and total riparian scale, although we did see slightly stronger effects of total riparian conditions vs stream reach on B-IBI.
An additional finding that I think is really interesting and important is that fine sediment from any source had a much larger effect on B-IBI than riparian conditions. In essence, we see a strong relationship between fine sediment impacts and B-IBI scores, but forest conditions don’t explain most of the variability that we see in our fine sediment data. This suggests that there are other mechanisms or sources of fine sediment that were not captured in the model. Furthermore, this sensitivity to sediment suggests that forested basins aren’t so different from urban streams in terms of the stressors they face.
It’s a logarithmic effect, so for every 171% increase in estimated fine sediments, we saw an 8-11 point decrease in B-IBI scores, and so that’s a pretty substantial effect.

## Slide 9: What does this mean?
Underperforming undeveloped basins probably not due to forest conditions
Notes: So what does this mean. The big take-home message is that the large variation in B-IBI scores that we see in undeveloped basins, can’t be explained by forest conditions alone in these basins.

## Slide 10: Study Questions
Do forest conditions influence biotic integrity?
  Yes, but effect size appears to be very small
What mechanisms and spatial scales?
  Sediment & leaf cover affect community structure
  Conditions nearest the stream have largest effect
  Total & stream reach conditions affect B-IBI scores
Notes: And so just to quickly re-cap our study questions, first, do forest conditions influence biotic integrity?
What we found is yes, but as measured in this study, the effect size appears to be very small.
Next, what are the mechanisms and spatial scales of that influence? The mechanism appears to be primarily through forest conditions influencing sediment and leaf cover, which, both of those in turn affect the community structure.
In terms of spatial scale, we found that the riparian conditions closest to the stream have the largest effect. And we also found that total and stream reach riparian conditions also affect B-IBI scores.

## Slide 11: Acknowledgements
Sampling Agencies:
  King County DNRP/Roads
  Snohomish County
  Clallam County
  Kitsap County
  Stillaguamish Tribal Nation
  Skokomish Tribal Nation
  Washington Department of Ecology
King County staff: Aaron David, Daniel Nidzgorski, Kate Macneale, Morgan Smith
Washington Department of Ecology
Puget Sound Partnership
Grant funded by US Environmental Protection Agency’s National Estuary Program