## Slide 1: Knotweed Biology and Control
Sasha Shaw
King County Noxious Weed Program

## Slide 2: Acknowledgements
Information in this presentation is based partly on:
  Controlling Knotweed (Polygonum cuspidatum, P. sachalinense, P. polystachyum and hybrids) in the Pacific Northwest
    by Jonathan Soll, The Nature Conservancy, 1/16/2004
Control recommendations and other details have been adjusted based on current information and the field experiences of our program and others in Washington State
For more details please see the original document at http://tncweeds.ucdavis.edu/esadocs/polybohe.html

## Slide 3: Why Worry About Knotweed?
Originally planted as an ornamental in the United States and Europe but now considered one of the worst invasive plants in riparian habitats
We have miles and miles of valuable riparian and wetland habitat that are vulnerable to knotweed invasion
It is one of the most difficult plants to eradicate growing in some of the most sensitive habitats

## Slide 4
Knotweed infesting a remote area on the upper Skykomish River
Knotweed

## Slide 5: What is Knotweed?
Tall, robust plants from Asia in the buckwheat family (Polygonaceae)
  Japanese knotweed (Polygonum cuspidatum, Fallopia japonica, Reynoutria japonica)
  giant knotweed (P. sachalinense)
  Bohemian knotweed hybrid (P. X Bohemicum)
Other common names:
  elephant ear bamboo
  false bamboo
  Mexican bamboo
  fleeceflower
http://www.dpi.vic.gov.au

## Slide 6: Japanese Knotweed (Polygonum cuspidatum)
Smaller than the others (6 feet usually)
Leaf bases are flat, not heart-shaped
Most clones in US are female (will have seeds later in season)
Flower clusters are longer and more ornamental

## Slide 8: Giant Knotweed (Polygonum sachalinense)
tallest species, up to 15 feet
leaves very large all with heart shaped bases
flower clusters shorter
most clones in US are female

## Slide 9
Giant knotweed in early spring with last year’s dead stems
Large leaves give giant knotweed its common name elephant ear bamboo

## Slide 10: Bohemian Knotweed (Polygonum X Bohemicum)
naturally occurring hybrid between the other two
most common type of knotweed found in the Pacific Northwest
medium tall (8 to 12 feet), mixed leaf shapes
introduced as an ornamental separately
most clones were male (flower clusters stiffly upright, no seeds)
recently females have been showing up with viable seeds (oh no!)

## Slide 11
Typical stand of Bohemian knotweed with stiffly upright male flower clusters

## Slide 12
Bohemian knotweed hybrid with seeds

## Slide 13: General Knotweed Characteristics:
Large, untoothed leaves, growing alternate on stems
Small white or greenish flowers grow in dense clusters from the leaf joints in July and August

## Slide 14
Young shoots in early spring look similar to red asparagus

## Slide 15
Japanese knotweed shoots emerge from rhizomes in April
http://www.oardc.ohio-state.edu/weedguide

## Slide 16
Hollow, upright, bamboo like stems often reddish or red-speckled

## Slide 17
Plants die back to the ground after hard frosts but hard, dry stems may persist through the winter

## Slide 18: How Knotweed Grows
Starts growth in April, later in colder areas
Grows extremely fast during the spring
  Giant knotweed can reach 15 feet by late June
  Bohemian knotweed reaches “only” 10 feet or so
Stems from deeply buried roots may emerge in late summer
Young giant knotweed stems

## Slide 19: How Knotweed Grows, cont.
Upward growth slows in July and is much reduced after August, when most of the growth is underground
Dies back to the ground with the first hard frost, and returns each spring from the same root system
When knotweed is cut or damaged, it vigorously and rapidly resprouts from latent buds on root crowns and rhizomes
Roots can spread 20 feet from the parent plant and go 7 feet down into the soil

## Slide 20
How knotweed grows and spreads (http://www.knotweed.co.uk)
Notes: Starts growth in April, full height by June (10-15 ft)
Rhizomes spread 20 feet or more from parent and go as deep as 7 feet
Root and stem fragments as little as ½ inch can form new plants
Seasonal floods move and break up plants and rhizomes, allowing them to colonize exposed gravel bars and streamsides
Perennial - spreads mainly by fragments
Sections 5 cm or longer produce shoots
Extensive rhizomatous mats - 5 meters deep
Also spreads in contaminated fill
Outgrows and shades out natives and other plants

## Slide 21: How Knotweed Reproduces
Seedlings occur but are uncommon
Mostly reproduces by vegetative means
  Root and stem fragments, as small as 1/2" can form new plant colonies
  Cut or broken stems and roots will sprout if left on moist soil or put directly into water

## Slide 22: How Knotweed Spreads
Fragments are spread by floods or high water, beavers, earth moving equipment, and in contaminated fill material
  Seasonal high water events and floods sweep plants into rivers and creeks, then fragment and disperse knotweed plant parts throughout the floodplains and cobble bars
  Roadside ditches, irrigation canals, and other water drainage systems can be colonized the same way

## Slide 23: Knotweed Invasion on Rivers
Knotweed rapidly spreads along rivers as fragments get moved by floods and grow into new clones downriver
Notes: Starts growth in April, full height by June (10-15 ft)
Rhizomes spread 20 feet or more from parent and go as deep as 7 feet
Root and stem fragments as little as ½ inch can form new plants
Seasonal floods move and break up plants and rhizomes, allowing them to colonize exposed gravel bars and streamsides
Perennial - spreads mainly by fragments
Sections 5 cm or longer produce shoots
Extensive rhizomatous mats - 5 meters deep
Also spreads in contaminated fill
Outgrows and shades out natives and other plants

## Slide 24
Despite knotweed’s large rhizome mass, it provides poor erosion control

## Slide 25: How Knotweed Takes Over
Colonizes flood-scoured shores and islands and other exposed areas
Emerges early in the season and quickly out-grows and shades out other plants
  inhibits even trees such as alder and willow
  understory of knotweed is usually bare of any other plants

## Slide 26: Knotweed Control Issues
It’s possible but takes dedication and commitment
  Eradication is likely to take several years and multiple treatments
Landscape level control requires long term planning and follow up
  Need to work from the top of the waterway down including tributaries
  Landscape level projects and large sites will almost certainly require integrating herbicide use into a control strategy
  Landscape level projects may be easier with an umbrella coordination effort such as a CWMA

## Slide 27: Knotweed Control Issues
Outreach and volunteer recruitment and coordination will improve the success of large landscape level projects
  Reach out to all public and private landowners
  Educate the broader community
Grants are available for invasive removal that benefits public resources
  especially for work done through non-profit organizations or government agencies (competitive but still worth trying!)
  County grants: through DNRP
  State grants: WSDA Knotweed Program
  Federal grants: US Fish and Wildlife, Forest Service
  Private foundations and corporations

## Slide 28: Knotweed Control Methods
Manual
Mechanical
Shade
Chemical
Combination

## Slide 29: When To Use Manual Methods
Easy site access
Patches are small (50 stems or less)
You can commit to following an intensive control regimen
You don’t intend to use stem injection method since repeated cutting tends to produce numerous small stems, too small to inject

## Slide 30: Manual Control Issues
Cutting and pulling stimulates shoot growth and depletes the roots
The more shoots there are per linear foot of root, the more likely you will be to be able to physically pull the roots out, exhaust them by depriving them of energy (i.e. by cutting the shoot off) or finish them off with an herbicide treatment

## Slide 31: Digging
Dig up as much root as possible in August over at least three consecutive years
Reported to work for small, isolated patches
Be sure to carefully dry or dispose of the roots
Do not put roots in a compost pile
  In England, soil contaminated with knotweed roots is considered an environmental contaminant and needs to be buried 10 feet deep
Be sure to search at least 20 feet away from the original patch center

## Slide 32: Digging knotweed up is possible but roots may go down 7 feet deep and extend out 20 feet and re-sprouting is likely
Notes: Cutting alone: twice a month between April and August, once a month after that until the first frost; for three years; don’t let stems exceed 6 inches
Cut material should be removed and dried; do not allow it to get into waterways
Digging/pulling in soft soil: similar to cutting in effectiveness, but careful work will improve success; dry out or dispose of roots; search at least 20 feet from each plant for rhizomes
Covering does not work alone, especially in areas where the covering can not be regularly monitored and maintained, but can help slow down re-sprouts

## Slide 33: Repeated Cutting
Cut stems close to the ground TWICE A MONTH OR MORE between April and August
And then cut once a month or more until the first frost
Repeat treatment every year for about 5 years
Try to keep plants from growing taller than 6 inches
Using a mower/weed-eater is an option if set close to the ground
Rake and pile up the cut stems where they will dry out, because stem fragments can root at the nodes
Do not allow cut, mowed or pulled vegetation to enter waterways

## Slide 34
Brush cutters often the first step in tackling a large stand of knotweed
Notes: Brushcutting: must be followed by foliar application of herbicide, or fabric
Cut once in June or July, then spray in the late summer or early fall when stems are 3 to 6 feet tall
Glyphosate or triclopyr; spray after flower buds form or several weeks to a month after mowing
Expect 2 to 3 years of treatment for 100% control; search at least 20 feet away for new shoots when re-treating sites; treat every leaf; may take several weeks to show impact

## Slide 35: The Four T’s of Manual Control
If you do try and control knotweed manually or mechanically, be sure you practice the four T’s:
  be Timely
  Tenacious
  Tough and
  Thorough

## Slide 36: Covering
Cover with heavy duty geotextile fabric or black plastic to starve the roots
Works better with isolated and smaller patches on open terrain
Plan to leave the covering material in place for three to five growing seasons
Try this right at the beginning of the year or after you’ve cut the plant down several times during the growing season and reduced some of the rapid plant growth

## Slide 37: Covering: How To
First cut stems down to ground surface and rake away stems or stomp on them to flatten as much as possible
Next cover the area with geotextile fabric or heavy duty black plastic expanding beyond the plant base and stems at least 10 feet beyond the outside stems
Use heavy rocks or stake and rope down the covering material as flat as possible; avoid putting holes in the fabric and overlap sections
Check fabric regularly, repair any damage and remove any emerging stems around edges

## Slide 38: Knotweed Control: Shade Cloth
Landscape fabric installed after cutting knotweed, staked and roped to secure. Note new sprouts coming up through holes.
Notes: Covering needs to be carefully monitored for sprouts through holes or overlapping layers.
Leave on for 5 years; can usually plant into the area after three.

## Slide 39: Chemical Control

## Slide 40: General Issues
Use an herbicide product labeled for your site
  e.g. aquatic, non-crop/right-of-way, home and garden, pasture, forestry
Follow label rates – more is not necessarily better!
Always read and follow label instructions
Use correct PPE
  At minimum: safety glasses, chemical proof gloves, long sleeves and pants, boots
May need an NPDES permit from Dept of Ecology or WSDA if there is any chance of herbicide getting into water

## Slide 41: Foliar Application
Can use backpack sprayer or large volume sprayer with hose
Risk of drift onto desirable vegetation and into water, soil
Easiest and fastest method
May be appropriate for roadside and large infestations where other methods aren’t possible
Expect some survival; repeat treatment for at least one to two years, possibly longer

## Slide 42: Timing
From flower bud to seeding: July through September
Short plants
  easier to reach with spray
  may not have enough leaf surface to absorb and translocate enough chemical to be effective
Taller plants
  more drift potential
  older plants may not be as efficient in translocating the chemicals
  harder to get complete coverage on tall plants
Best strategy may be to cut or bend stalks and allow to regrow to 3 to 6 feet tall
  Usually takes about 4 weeks or more

## Slide 43
Foliar spray to treat knotweed re-growth
Knotweed Control: Foliar Treatment
Notes: Sprayed regrowth from 2004 injected and sprayed sites. Regrowth too small to inject. Regrowth from sites treated by foliar application in 2004 was approx 10% - 15%.
Glyphosate or triclopyr; spray after flower buds form or several weeks to a month after mowing
Expect 2 to 3 years of treatment for 100% control; search at least 20 feet away for new shoots when re-treating sites; treat every leaf; may take several weeks to show impact

## Slide 44: Herbicide Types
Use systemic herbicide – goes from leaves to roots
Glyphosate: 2 to 8 % solution
  Non-selective – will harm all actively growing plants if leaves are sprayed; works well combined with imazapyr
  Aquamaster/Rodeo plus surfactant (LI-700, Agridex) - aquatic sites
  Roundup Pro (has surfactant mixed in) – non aquatic sites
Triclopyr: ¾ to 5% solution (lower concentrations result in better long term control, higher rates give good top kill)
  Selective – will not harm grass, rushes, cattails, etc
  Renovate – aquatic sites
  Garlon 3A – non-aquatic sites
Imazapyr
  the most effective available product for long-term knotweed control
  slow-acting and expensive; higher risk of off-target damage
  also effective in combination with glyphosate
  Habitat – aquatic
  Arsenal - non-aquatic sites

## Slide 45: Combo Method
In spring or summer, spray or cut/bend stems followed by fall foliar spray
Sets plants back so they can be sprayed at the appropriate growth stage and at the best height
Cutting first instead of spraying will reduce overall herbicide input into the watershed and is probably more labor efficient
  can use volunteers or crews without pesticide licenses for cutting or bending

## Slide 46: Stem Injection
Use stem injection gun or similar tool
  Also marker paint or marker and a cork for the needle
Follow directions carefully especially calibration and cleaning
  Inject 3 to 5 ml into stem between first and second nodes or between second and third node if too woody lower down
Timing best from mid-June to end of September
Currently only Aquamaster has a label for injection but Roundup Pro may also have it soon

## Slide 47
Injecting herbicide directly into the stems of knotweed
Knotweed Control: Stem Injection
Notes: Injection: 3ml dose per cane of Glypro (aquatic formulation of Glyphosate). Findings show 5 % regrowth in subsequent years. In 2005, spent 15 days of crew time injecting on the Green River and Soos Creek (hatchery Park).

## Slide 48: Pros of Stem Injection
Highly effective: over 90% controlled in first year
Greatly reduces drift and highly selective
No cut stems to deal with

## Slide 49
Dead knotweed canes following treatment with stem injection gun

## Slide 50: Cons of Stem Injection
Very time and labor intensive compared with foliar spraying
Need to inject every cane in the stand
Glyphosate label typically 2 gallons per acre so can only inject about 2500 stems per acre
Can only inject stems over ½ inch so there will always be small stems that can’t be injected in a population, especially in the second year of treatment

## Slide 51: Cut Stem/Pour Application
Similar to stem injection, may not be as effective
May be good for small patches and greatly reduces drift
Cut stems between lowest 2 nodes
3 ml undiluted (concentrated) glyphosate into stem cavity
  Can use a large needle with measured reservoir to be precise
  Be very careful not to splash out onto the ground
Follow label directions on amount applied per acre
  for the 2 gallons per acre label can only inject 2500 stems/acre
Timing best in late summer or early fall
Need to remove cut stems away from water where they can dry out and not spread off site

## Slide 52: Wick Wipe Method
Uses an applicator with a sponge on the end of a reservoir for the herbicide
Use glyphosate or triclopyr at 33 to 50 % concentration
Greatly reduces drift
Hard to get chemical on leaf surface and seems to increase personal contact with herbicide

## Slide 53
Applying herbicide to knotweed leaves with a wick wiper

## Slide 54: Useful Websites
The Nature Conservancy Wildlands Invasive Species Website: Knotweed Page
  http://tncweeds.ucdavis.edu/esadocs/polybohe.html
Washington State Department of Agriculture Knotweed Program
  http://agr.wa.gov/PlantsInsects/Weeds/Knotweed/Knotweed.htm)
Stem-injection tool information and ordering
  http://www.jkinjectiontools.com
Aquamaster label/supplemental label
  http://www.monsanto.com/ito/products/aquamaster.html

## Slide 55: Info on Noxious Weeds in King County:
http://kingcounty.gov/weeds
Weed Photo Page:
Search by Weed Name
Click thumbnail picture to get more information and photos

## Slide 56: Sasha Shaw King County Noxious Weed Program 201 South Jackson St, Suite 600 Seattle, WA 98104 206-263-6468 sasha.shaw@metrokc.gov www.kingcounty.gov/weeds